## Slide 1
CANopen
Length meter Protocol
DAS Co., Ltd.

## Slide 2
< Review of functions >
The inclinometers are equipped with a standardized CANopen interface per CiA DS-301 and a device profile per CiA DSP-410. All measurement values and parameters are accessible via the object register (OR). The individual configuration can be stored in the internal, non-volatile memory buffer (EEPROM).
The following CANopen functions are available:
one Send Data object (TPDO1) with four possible operating modes:
- individual request per Remote Transmit Request telegram (RTR)
- cyclic Send per interval time
- event-driven Send when angle has changed
- synchronized Send after receipt of SYNC telegram
one Service Data object (Standard SDO)
error messages per emergency object (EMCY) with the help of:
- the general error register
- the manufacturer specific status register (Manufacturer Status)
- the error list (Predefined Error Field)
storage and reload function of all parameters (Store and Load Parameter Field)
Failure Monitoring
setting of Node ID, as well as Baud rate per OR
freely configurable limit frequency (digital filter)
configuration of minimal change of angle for TPDO1 send event
< Send PDO (TPDO1) >
Each inclinometer has exactly one Send Process Data Object (TPDO). It contains the current inclination values (longitudinal and lateral). PDO mapping of measurement values is fixed as displayed in Table 1.
Table 1. PDO mapping of TPDO1
* DATA : angle = [signed 16] , Length = [unsigned 16]

## Slide 3
< PDO communication types >
Individual request per Remote Transmit Request telegram (RTR)
A request can be sent to TPDO1 anytime by sending a Remote Transmit Request telegram. This is possible in all operating modes of the inclinometer.
Cyclic operating mode
Cyclic sending of TPDO1 is activated if the entry 1800h/05h (interval time in milliseconds) contains a value greater than 0.For this purpose the entry 1800h/02h (transmission type) must contain the value 254 (asynchronous, manufacturer specific). In the Operational mode, the inclinometer cyclically sends the TPDO1 with the set cycle duration time.
Event-driven Send when the angle has changed
The bus load caused by PDOs can be decreased by only sending the TPDO1 when the angle has changed accordingly. This function can be configured under the index 3001h in the manufacturer specific portion of the object register. For this purpose the entry 1800h/02h (transmission type) must contain the value 254 (asynchronous, manufacturer specific).
Synchronized Send after receipt of a SYNC telegram
For the synchronized transmission, the SYNC object is made available by CANopen; here, the TPDO1 is sent after each „nth“ receipt of a SYNC telegram. For this purpose the entry 1800h/02h (transmission type) must contain the value n=1...240.
< Object register >
The object register of the inclinometers is divided into three parts (communication parameters, manufacturer specific portion, profile specific portion). The existing parameters can be read and written via the Standard SDO and index/subindex. Parameter changes become immediately valid with the exception of the Node ID (2000h) and the Baud rate (2001h).
The following paragraphs provide a description of all parameters in the object register of an inclinometer including index, subindex, data type, access rights and standard value (manufacturer default setting). The column Store identifies whether a parameter can be stored in the internal, non-volatile memory buffer (write„save“ signature in OR index 1010h/01h).

## Slide 4
Index | Sub-index | Parameter | Data type | Access | Standard value | Store
1000h | 0 | Device type (device proﬁle 410, two axes) | UNS32 | const | 2019Ah | 
1001h | 0 | Error register | UNS8 | ro | 0 | 
1003h | Predeﬁned error ﬁeld |  |  |  |  | 
 | 0 | Number of error entries | UNS32 | rw | 0 | 
 | 1...5 | Error code (oldest error in highest index) | UNS32 | ro | 0 | 
1005h | 0 | COB ID SYNC message | UNS32 | rw | 80h | 
100Ah | 0 | Software version (“xyy”) | VSTR | const | typical | 
1010h | Store parameters |  |  |  |  | 
 | 0 | Highest supported subindex | UNS32 | ro | 1 | 
 | 1 | Store all parameters (signature: “save”- 65766173h) | UNS32 | rw | 0 | 
1011h | Reload manufacturer default setting |  | UNS32 |  |  | 
 | 0 | Highest supported subindex | UNS32 | ro | 1 | 
 | 1 | Reload all manufacturer default settings (signature: “load”- 64616F6Ch) | UNS32 | rw | 0 | 
1014h | 0 | COB ID emergency message | UNS32 | ro | 80h+NID | 
1015h | 0 | Oﬀ-time between two EMCY messages (a multiple of 100 μs) | UNS16 | rw | 0 | x
1017h | 0 | Heartbeat interval time (a multiple of 1 ms, 0 deactivated) | UNS16 | rw | 0 | x
1018h | Identity object |  |  |  |  | 
 | 0 | Highest supported subindex | UNS8 | ro | 4 | 
 | 1 | Vendor ID | UNS32 | ro | 0h | 
 | 2 | Product code | UNS32 | ro | typical | 
 | 3 | Revision No. | UNS32 | ro | typical | 
 | 4 | Serial No. | UNS32 | ro | typical | 
1200h | Server SDO1 parameter |  |  |  |  | 
 | 0 | Highest supported subindex | UNS8 | ro | 2 | 
 | 1 | COB ID Client > Server | UNS32 | ro | 600h+NID | 
 | 2 | COB ID Server > Client | UNS32 | ro | 580h+NID | 
1800h | Transmit PDO1 communication parameters |  |  |  |  | 
 | 0 | Highest supported subindex | UNS8 | ro | 5 | 
 | 1 | COB ID | UNS32 | ro | 180h+NID | 
 | 2 | Transmission type (synchronous / asynchronous manufacturer speciﬁc) | UNS8 | rw | FFh | x
 | 3 | Oﬀ-time between two TPDO messages (a multiple of 100 μs, 0 deactivated) | UNS16 | rw | 0 | 
 | 4 | Compatibility entry | UNS8 | rw | 0 | x
 | 5 | Interval time for cyclic Send (a multiple of 1 ms, 0 deactivated) | UNS16 | rw | 0 | x
< Communication parameters (per CiA DS-301) >

## Slide 5
Error register (1001h)
The error register displays the general error status of the device. Each Bit represents an error group. If a Bit is set (=1), at least one error of this group remains active at this time.
The content of this register is transmitted in each EMCY message. The following error groups may occur:
Bit 7...Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2...Bit 1 | Bit 0
Not used | Proﬁle speciﬁc error | Not used | Temperature error | Not used | At least one error active
If the device remains in the error status (at least one error active), it is displayed by set Bit 0.
During active monitoring of the internal device temperature (5001h/01h = 1), Bit 3 is set when set limit values (5001h/02h...03h) have been underreached or rather overreached.
A profile specific error (sensor error) is displayed by Bit 5.
Predefined error field (1003h)
Each inclinometer compiles an error list concerning the five errors that have occurred last.
The entry 1003h/00h contains the number of error entries in the error field. All other subindices contain all occurred error states in chronological sequence; the error that has occurred last may always be found under subindex 01h. The oldest error may be found in the highest subindex (value of 1003h/00h) available and is removed first from the list when more than five errors have occurred. If an error occurs, a new error entry is added to 1003h and an EMCY message is sent as well.
An erorr entry is structured as follows:
Additional information ﬁeld (Bit 31...Bit 16) | Error code (Bit 15...Bit 0)
Bit 15...Bit 0 of the manufacturer status register 1002h (at the time the error has occurred) | 4200h (temperature error) 5000h (hardware error) FF00h (device speciﬁc error)
The error list may be completely deleted by writing 0 into the entry 1003h/00h.
Store parameters (1010h) and reload (1011h)
If parameters are changed in the OR, the changes become immediately valid with the exception of Node ID (200h) and Baud rate (2001h). The changed parameters must be stored in the internal EEPROM so that they remain active after a reset. By writing the signature „save“ (65766173h) into the entry 1010h/01h all active parameters of the OR are sent to the non-volatile memory buffer.
The OR may be reset to the manufacturer default via the entry 1011h/01h and by writing the signature„load“ (64616F6CH) into this entry. Thus the default parameters are written into the non-volatile memory buffer with the exception of the Node ID
(2000h) and the Baud rate (2001h). After a „reset application“ (NMT command) or rather a hardware reset, the changes become valid; if only a „reset communication“ (NMT command) is sent, only the default settings of the communication parameters become valid.
After the„save“ and„load“ command, a reset should not occur for a minimum time period of approx. one second; this ensures that the parameters are correctly stored in the EEPROM.
Storing device parameters in the internal EEPROM may take a relative long time. This is why the „save“ and „load“ commands are immediately answered, but storing is executed retroactively and„in addition to.“

## Slide 6
< Transmit PDO1 – transmission type (1800h) >
With the help of the entry 1800h/02h it can be determined how sending the PDOs is to be initiated.
Transmission type | Description
1...240 | Synchronous (cyclic) Only synchronized transmission via SYNC possible
254 | Asynchronous, manufacturer speciﬁc Cyclic operating mode and/or send when angle has changed can be activated via respective conﬁguration.
Manufacturer specific portion
Index | Sub -index | Parameter | Data type | Access | Standard value | Store
2101h | 0 | Node ID (1...127) | UNS8 | rw | 10 (0Ah) | x
2102h | 0 | Baud rate (in kBit/s) | UNS16 | rw | 250 | x
3000h | 0 | Limit frequency digital ﬁlter (0 = deactivated or 300...25000, in mHz) | UNS16 | rw | 3000 | x
Node ID (2000h) and Baud rate (2001h)
After a change has occurred, the Node ID and the Baud rate only become valid after a reset (reset application, reset communication and hardware reset). This is why the two parameters must be transferred to the EEPROM with the save command (1010h/01h) after a change has occurred. After a reset, all COB IDs are recalculated and reset according to the predefined connection set.
The Baud rate is set in kBit/s. { 10, 20, 50, 125, 250, 500, 800, 1000 }
Limit frequency digital filter (3000h)
The inclinometer offers the possibility to render continually forming angle values insensitive against external, interfering vibration. With the help of a parameterizable low-pass filter parasitic vibrations may be suppressed. The limit frequency may be set individually between 0.3 and 25 Hz. The digital filter inside the sensor is a Butterworth Low-pass 8th Order. Values of 300 (= 0.3 Hz) to 25000 (= 25 Hz) are thereby permissable. The digital filter is deactivated by the value 0.

## Slide 7
< Emergency messages >
Each inclinometer supports EMCY messages which are sent in case of sensor, temperature, hardware or guarding errors. If one of these errors occurs, the OR entries 1001h (Error Register), 1002h (Manufacturer Status Register) and 1003h (Predefined Error Field) are activated (please refer to paragraphs Error register (1001h) and Predefined error field (1003h)).
After an error has been corrected, the device sends an EMCY message with the„error reset“ code (0h) and the current status of the error register, as well as the manufacturer status register. The current device status („pre-operational, operational or stopped“) is not impacted by the error states except by the guarding error.
EMCY message protocol
- EEC (Emergency error code) - see Table EEC
- ER (Error Register) - see Table ERA
- EB (Error bits) - see Table EB
Table EEC – Emergency error code
ID | byte0 | byte1 | byte2 | byte3 | byte4 | byte5 | byte6 | byte7
80h + Node ID | EEC |  | ER | EB | Not used |  |  | 
Code | Description
0000h | Error reset or no error
1000h | Generic error
6100h | Internal software – generic
8100h | Communication – generic
8110h | CAN overrun (objects lost)
8120h | CAN in error passive mode
8130h | Life guard error or heartbeat error
8140h | recovered from bus off
8200h | Protocol error - generic
8240h | Unexpected SYNC data length

## Slide 8
Table ER – Error register
Table EB - Error bits
Code(bits) | Description
00h | Generic error
01h | Current
02h | Voltage
04h | Temperature
08h | Communication error
10h | Device profile specific
20h | Reserved(always 0bit)
40h | Manufacturer specific
Code(bits) | Description
00h | No error
01h | CAN bus warning
06h | CAN receive bus passive
07h | CAN transmit bus passive
12h | CAN transmit bus is off
14h | CAN receive buffer has overflowed
18h | SYNC message timeout
19h | Unexpected SYNC data length
1Ah | Error with PDO mapping
20h | Emergency buffer is full

## Slide 9
< Failure monitoring >
Failure monitoring functions Heartbeat monitoring methods can be used.
< Heartbeat >
Heartbeat is a failure monitoring mechanism which functions without RTR telegrams.
For this purpose the inclinometer cyclically sends a Heartbeat message which contains the status of the device. The master is able to monitor these telegrams. Heartbeat is activated as soon as a value greater than „0“ is entered into the register Heartbeat Interval Time (1017h).
< COB Ids >
The CAN identifiers of the communication objects are set according to the predefined connection set at each reset (communication, application and hardware reset) depending on the preset Node ID (2000h). Table 10 displays the basis for calculation and example values (Node ID = 10).
Communication object | Calculation of COB ID | Example value (Node ID = 10)
NMT | 0h | 0h
SYNC | 80h | 80h
EMCY | 80h + Node ID | 8Ah
TPDO1 | 180h + Node ID | 18Ah
Standard SDO (Client > Server) | 600h + Node ID | 60Ah
Standard SDO (Server > Client) | 580h + Node ID | 58Ah
Heartbeat | 700h + Node ID | 70Ah
< EDS files >
An electronic data sheet (EDS file) is available for each inclinometer (download free of charge from the internet under http://www.das-co. com...).
It contains a complete description of the object register and can be easily added to a CANopen project planning software.